Abstract

Introduction

The performance of any real-time control system is only as good as the hardware it runs on. Reliably fast processing is critical not only to enable high frequency sampling but also to reduce noise created by jitter. If samples are not evenly spaced in time, calculations on the rate of change of signals will be inaccurate.

Field Programmable Gate Arrays (FPGAs) are a key tool in control and data acquisition due to their performance and reconfigurability. Direct hardware access means high levels of control over timing, which means a fast and deterministic control loop. Reconfigurability makes rapid prototyping possible and allows the FPGA to be updated for compatibility with different connected peripherals.

The cost of this performance is complexity. Designers need to specifically engineer functionality that is packaged into other tools and made simple through abstraction. Their parallel nature makes FPGA programming sufficiently different to programming a processor that many more common programming skills are not transferable. Uliana, D. et al. (2013) state that “most non-engineer domain experts lack the skills needed” to create efficient and robust designs.

Pynq toolchain. Python interface for FPGA designs. Python widely spoken 18.2 million developers (Korakitis, K. et al., 2024), lots of resources, like natural language. The framework makes it possible for Python programmers to read and write registers on a connected FPGA. It also allows for pre-compiled designs called bitstreams to be loaded onto the FPGA without using FPGA-specific tools. This gives non-specialist users the ability to customise FPGA designs using code written by in-house or community specialists.

The performance of FPGAs “make them especially suitable [as an interface to] an ultra-high speed ADC” (Sisterna, C. et al, 2011). Analogue to Digital Conversion is necessary to convert analogue signals from a plant so they are compatible with a digital controller. Despite being “a common engineering challenge” (Analog Devices, 2019), it is work that developers frequently repeat.
ADCs have a wide range of different parameters that mean they need distinct interfaces. ADCs have a variety of interface styles “depending on the application and speed”(Gupta, S. and Kumar, S, 2018). While these interfaces are sometimes standardised “data transfer interfaces such as SPI, I2C, UART” (Suresh, A., 2024), some use specialised interfaces such as parallel Double Data Rate, JESD204 and SPORT.
A method of abstracting away the varying outputs of ADCs would simplify integration into projects. Designers would no longer need to study exactly how to operate each new model from datasheets. Non-specialists would be able to swap out the ADCs of a project without re-writing and compiling the FPGA design.
Market research reveals several universal inputs to ADCs – these are signal conditioning circuits to match the input to the ADC’s operating range – but nothing to set the output to a format readable by devices later in the loop. There are general purpose methods of handling common serial communication protocols such as I2C and SPI in FPGAs, and these could serve as an interface to a large share of available ADCs. For example, dedicated Microblaze soft processors can handle SPI and I2C communications (Naidu, T. and Solanki, D., 2022). Microblaze drivers designed to handle these communication protocols are freely available.
This project aims to explore the feasibility of an interface in which partial reconfiguration is leveraged for compatibility with all ADCs, without rebuilding the FPGA design. When the idea was proposed to the PYNQ community forum, a moderator commented that “there is value in such a project” (Ruiz, M., 2025).
The universal interface will be developed on a PYNQ Z1 development board. It features an ARM processor embedded onto the FPGA which is capable of reprogramming parts of the FPGA design. The design will feature an AXI stream capable of moving data from the Programmable Logic (PL) to the Processing System (PS) via Direct Memory Access (DMA). The input to the AXI stream will be data from an ADC. The interface to this ADC will be settable via a Python user interface running on the PS, which reprograms part of the FPGA design to include the selected interface through partial reconfiguration. The same Python interface shall then acquire and process the ADC data.

Aims and Objectives
This project aims to produce a universal ADC interface in order to test the feasibility of such a device. By following the design process through from the beginning any unforeseen obstacles will be uncovered.
To do this, the following objectives will be met:
Create an interface capable of swapping between at least two ADC interface standards.
Develop a Python user interface to be able to set the model of ADC in use.
Identify any factors that could limit the type and number of ADCs compatible with this system.
Analyse scalability to predict the effect of adding compatibility with hundreds of different models of ADC.
Evaluate the ease of use of the system to a developer with no prior experience of FPGA tools.

Methodology
Design Overview
A key technology in enabling this project was the PYNQ framework. The framework provides Python wrappers that allow for full and partial bitstreams to be loaded from the PS. While none of the techniques used in the project are impossible to implement without the framework, development time was shortened by using the pre-configured tools.
To compliment the Python workflow offered by PYNQ, cocotb was used for testbenching each module of the design in software. Cocotb is a tool that interacts with a running simulation of an FPGA module using Python. Software tests can be written more quickly and clearly than is possible with other testbenching tools. This accelerated debugging and verification of each design unit.
In the case of both PYNQ and cocotb, debugging interactively with the Python debugger was an unforeen benefit that smoothed the process of stepping through VHDL logic.
A method of streaming data from the PL to the PS is convenient to prove that the data generated by the ADC interfaces is correct. The PS would often be responsible for offloading data to the rest of the control loop. For example, on the PYNQ-Z1 development board used for this project the Ethernet hub is hard-wired to a PS pin – in other words, data sent over Ethernet must route through the PS on this board.
Communication from PL to PS is possible through interfaces exposed by the PS. These consist of General Purpose I/O (GPIO) and AXI ports which facilitate Memory Mapped I/O (MMIO) and Direct Memory Access (DMA). Some ADCs generate data at a high rate therefore the technique best suited for high data throughput was selected to pass data from the PL to the PS. This technique is DMA <citation needed>.
It is convenient to be able to configure the PL side from the operating system running on the PS. This necessitates PS to PL communications. GPIO pins are useful for simple applications such as resets and triggers. The PS features an SPI bus that would be useful for passing short pieces of configuration data, but accessing it requires editing the device tree. The best supported option seems to be MMIO, and so it is commonly the communication link used in the project. <citation needed>
DMA is handled by a Vivado IP. On the development board, the PL is already connected to the block of memory that the PS uses as RAM. The Vivado IP writes to a specified memory buffer data that is passed to it via the AXI Stream protocol (AXIS).
A First-In-First-Out buffer (FIFO) is used to store data before it is consumed by the PS in a DMA write operation. Using a FIFO means that the DMA operations do not need to be synchronised to the ADC completing each sample. This reduces the complexity of the system but also makes it more general to the various types of ADCs it might need to be compatible with. Larger writes of many samples demand less of the processor than continuously reading values because it has to less frequently update the DMA with instructions. Therefore the FIFO allows the system to run more efficiently.
These Vivado IPs were used because they reduced development time and reduced likelihood of bugs or errors in this part of the design. However, these IPs are closed source and so the modules cannot be customised. For example, the depth of the FIFO cannot be configured after compilation through an MMIO interface. This does not effect compatibility with all ADCs but should be noted that changing these parameters would require recompilation by a specialist with access to the Vivado tools.
AXI interfaces to fill the FIFO with ADC data must be written per ADC. Interface clocking signals are first sent through a PS configurable clock divider which ultimately controls the sample rate of the ADC. Each interface is connected to an AXI-Lite bus so configuration data can be accepted via MMIO. It is also connected to an AXIS bus to pass data out to the FIFO.
The PS must also set the number of samples to send before raising TLAST. Experimentation revealed a DMA transfer does not complete when the FIFO is emptied, but instead continues to wait for data to come from the FIFO until either the buffer the DMA writes to is full or the TLAST marked packet is received. This gives TLAST similar behaviour as setting the buffer size. Increasing the number of packets before TLAST is raised increases latency but decreases computational load and vice versa.
The interface is also responsible for triggering the interface to collect samples from the ADC until TLAST is raised. In other words, the interafce does not continually feed the FIFO with data because the FIFO would fill with data that might not be useful. This risks the FIFO becoming full if it is not drained frequently enough by the PS and potentially valuable data being lost. It also means that the user has no way of telling the difference between data they wish to acquire and data that was already filling the FIFO. By including a trigger the user can choose to only capture data near a significant event.
The FIFO is configured to accept data 32 bits in width so the interface is required to package ADC readings in groups of 32 bits. During testing, zeroes were simply prepended to each sample to make up the extra bits. This does waste some bandwidth of the stream to PS memory. An initially planned optimisation was to only mark relevant bits for transmission with the TKEEP signal. While the FIFO does support using TKEEP to mark a subset of TDATA as valid, this is not supported by the DMA module.
The PYNQ framework includes firmware to abstract the process of interacting with the logic running on the PL. It does this by parsing a Hardware Hand-off File which is generated by Vivado along with the bitstream to program the FPGA. This file provides information about what modules are present in the design, their location in the bitstream and their addresses on the memory map. The PYNQ tools consist of Python libraries for common IPs including methods to read and write registers on those IPs via MMIO.
Working in this way enables the user to control things like the DMA with a few basic Python commands. This was initially done interactively from the command line while experimenting, which is already a useful feature because with each step a user can inspect the state of the device in a way that is easier than with compiled code. Eventually a script was written to automate the steps required and it came to just 7 lines of Python code.
PYNQ also provides an SD card image containing an operating system for the PS with a Jupyter server pre-configured to start at boot. While there are many Python tools that could be leveraged to act as a user interface and to graph results, this support for Jupyter notebooks make them an attractive option. A notebook was written that uses interactive widgets to function as a user interface and matplotlib to graph the output of the ADC.
The first interface written in VHDL was not for an ADC at all. It is a test module that outputs a counter into the FIFO. Apart from being immediately useful as a way to see data coming through on the PS and confirming that the design up until this point works as intended it serves as the default module when the FPGA first boots up. Until the user selects the ADC they wish to use, this module will be adding zeroes to the FIFO so that if the user tries to do a DMA read they will receive zeroes rather than triggering an error in the DMA.
Following this, an interface was created for an SPI-based ADC, an MCP3008. For each sample, the ADC transmits 5 bits of configuration data to the ADC through SPI and then reads back 10 bits of data. The data is packaged and exposed on an AXI TDATA port ready to send to the FIFO. The configuration information sent to the DMA can be set via MMIO in the PS. The ADC has 8 channels that can be selected from and can operate in either differential or single-ended mode. <datasheet link?>
With these two sources of data tested and working

Why not Microblaze?
- Key differences

Tried with PR
Vivado RTL flow.
What connects to GPIO pins? Should be AXI-Lite? SPI? Could connect to SPI bus?
- ADC sample rate
- All the control lines – channel, diff, DAC to Vref? Start
- For faster rate, interrupts better than polling when FIFO nearly full
- tkeep from AXI. Send fewer zeroes

Technical Analysis (gathering results)

Time taken for dynamic reconfiguration
Scalability
335 primatives – 129 flop latches and 182 Look Up Tables (LUTs). Microblaze has about 950 LUTs (https://adaptivesupport.amd.com/s/article/11920?language=en_US)
Bitstreams use 4 MB for static overlay and 327 kB for each reconfigurable module.
- Doesn’t actually save output pins
Ease of use – button clicks and time taken
Coverage
- LVMOS should be fine
- Flexibility of control lines?

Results (Evaluate technical analysis)

Conclusions
Wouldn’t have to be PYNQ – cheaper solution possible (proof?)
Similar possible with MicroBlaze
Partial reconfig is powerful
- especially as no reboot required
ADC configuration is hard!

https://ieeexplore.ieee.org/abstract/document/6683952

https://www.monolithicpower.com/en/learning/mpscholar/analog-to-digital-converters/adc-interfaces-and-power-management/adc-output-interfaces?srsltid=AfmBOoqakkq7Gg6HpWljsgYFGfSmHp3RitZO986Fpz1Izll7U0kCJt-t (if not already in there?)

https://www.ti.com/lit/ug/sbau412a/sbau412a.pdf

Korakitis, K., Noll, B., Dodd, L., (2024) Sizing Programming Language Communities [online]. 26th edition. Manchester: SlashData. Available from: https://www.developernation.net/resources/reports/sizing-programming-language-communities/ [Accessed 10 March 2025]

https://docs.amd.com/r/2024.1-English/ug909-vivado-partial-reconfiguration/Implementing-the-DFX-Design

https://adaptivesupport.amd.com/s/article/11920?language=en_US Microblaze LUTs