The performance of any real-time control system is only as good as the hardware it runs on. Reliably fast processing is critical not only to enable high frequency sampling but also to reduce noise created by jitter. If samples are not evenly spaced in time, calculations on the rate of change of signals will be inaccurate.

Field Programmable Gate Arrays (FPGAs) are a key tool in control and data acquisition due to their performance and reconfigurability. Direct hardware access means high levels of control over timing, which means a fast and deterministic control loop. Reconfigurability makes rapid prototyping possible and allows the FPGA to be updated for compatibility with different connected peripherals.

The cost of this performance is complexity. Designers need to specifically engineer functionality that is packaged into other tools and made simple through abstraction. Their parallel nature makes FPGA programming sufficiently different to programming a processor that many more common programming skills are not transferable. Uliana, D. et al. (2013) state that “most non-engineer domain experts lack the skills needed” to create efficient and robust designs.

Pynq toolchain. Python interface for FPGA designs. Python widely spoken <user number!>, lots of resources, like natural language. The framework makes it possible for Python programmers to read and write registers on a connected FPGA. It also allows for pre-compiled designs called bitstreams to be loaded onto the FPGA without using FPGA-specific tools. This gives non-specialist users the ability to customise FPGA designs using code written by in-house or community specialists.

The performance of FPGAs “make them especially suitable [as an interface to] an ultra-high speed ADC” (Sisterna, C. et al, 2011). Analogue to Digital Conversion is necessary to convert analogue signals from a plant so they are compatible with a digital controller. Despite being “a common engineering challenge” (Analog Devices, 2019), it is work that developers frequently repeat.
ADCs have a wide range of different parameters that mean they need distinct interfaces. ADCs have a variety of interface styles “depending on the application and speed”(Gupta, S. and Kumar, S, 2018). While these interfaces are sometimes standardised “data transfer interfaces such as SPI, I2C, UART” (Suresh, A., 2024), some use specialised interfaces such as parallel Double Data Rate, JESD204 and SPORT.
A method of abstracting away the varying outputs of ADCs would simplify integration into projects. Designers would no longer need to study exactly how to operate each new model from datasheets. Non-specialists would be able to swap out the ADCs of a project without re-writing and compiling the FPGA design.
Market research reveals several universal inputs to ADCs – these are signal conditioning circuits to match the input to the ADC’s operating range – but nothing to set the output to a format readable by devices later in the loop. There are general purpose methods of handling common serial communication protocols such as I2C and SPI in FPGAs, and these could serve as an interface to a large share of available ADCs. For example, dedicated Microblaze soft processors can handle SPI and I2C communications (Naidu, T. and Solanki, D., 2022). Microblaze drivers designed to handle these communication protocols are freely available.
This project aims to explore the feasibility of an interface in which partial reconfiguration is leveraged for compatibility with all ADCs, without rebuilding the FPGA design. When the idea was proposed to the PYNQ community forum, a moderator commented that “there is value in such a project” (Ruiz, M., 2025).
The universal interface will be developed on a PYNQ Z1 development board. It features an ARM processor embedded onto the FPGA which is capable of reprogramming parts of the FPGA design. The design will feature an AXI stream capable of moving data from the Programmable Logic (PL) to the Processing System (PS) via Direct Memory Access (DMA). The input to the AXI stream will be data from an ADC. The interface to this ADC will be settable via a Python user interface running on the PS, which reprograms part of the FPGA design to include the selected interface through partial reconfiguration. The same Python interface shall then acquire and process the ADC data.

Aims and Objectives
This project aims to produce a universal ADC interface in order to test the feasibility of such a device. By following the design process through from the beginning any unforeseen obstacles will be uncovered.
To do this, the following objectives will be met:
Create an interface capable of swapping between at least two ADC interface standards.
Develop a Python user interface to be able to set the model of ADC in use.
Identify any factors that could limit the type and number of ADCs compatible with this system.
Analyse scalability to predict the effect of adding compatibility with hundreds of different models of ADC.
Evaluate the ease of use of the system to a developer with no prior experience of FPGA tools.

https://ieeexplore.ieee.org/abstract/document/6683952

https://www.monolithicpower.com/en/learning/mpscholar/analog-to-digital-converters/adc-interfaces-and-power-management/adc-output-interfaces?srsltid=AfmBOoqakkq7Gg6HpWljsgYFGfSmHp3RitZO986Fpz1Izll7U0kCJt-t (if not already in there?)

https://www.ti.com/lit/ug/sbau412a/sbau412a.pdf